## Slide 1: SPARK – 2021 Internship @ IITR Probabilistic seismic resilience model for spatially distributed systems
By:
Rajat Shakya
Under the Guidance of
Prof. Saurabh Shiradhonkar

## Slide 2: Problem Statement
If there are N spatially distributed bridges, in a seismically active region, how do we determine which bridge to retrofit first?
To develop a framework that will allow the decision on priority of retrofit to be made based on:
- Level of seismic hazard
- Performance of Bridge
- Expected Loss
- Recovery after occurrence of damaging event
Picture Source: Google Maps

## Slide 3: PSHA and Hazard Curve
Seismic Hazard
  Probable level of ground shaking associated with the recurrence of earthquakes (Shedlock, 2002)
  Measured as Peak Ground Acceleration and/or Spectral Acceleration
Probabilistic Seismic Hazard Assessment
  Total hazard due to all possible earthquake scenarios using their probabilities. (Baker, 2008)
  Output is Hazard Curves
    Relates Hazard at each location with the frequency of exceedence
Figure Source: USGS Unified Hazard Tool
Fig. Typical Hazard Curves for a location

## Slide 4: Generation of Scenario Earthquakes from PSHA
The need:
  The losses and resilience calculation requires individual scenarios that affect the structure.
  Need to identify sources that affect all locations.
Deaggregation:
  Splitting of Hazard into contributing sources.
  Output is Sources, their contribution in %, and the magnitude, distance pair.
Figure Source: USGS Unified Hazard Tool
Fig. Typical Deaggregation Graph for a hazard
Fig. Typical Deaggregation Contributor Table for a hazard

## Slide 5: Estimation of Damage States of Bridges
The need:
  Losses from an event are incurred due to some damage caused by the event
  Expected damage can be translated to expected loss for an event
Fragility Functions
  Relates Hazard with exceedance probability of damage state
  Damage state associated with mean damage ratio
  Damage ratio: repair cost / replacement cost
**Hazards due to different sources are calculated using the Ground Motion Prediction Equations.
Source: HAZUS-MH MR3, 2003
Fig. Typical Fragility Curve for a structure

## Slide 6: Expected Seismic Losses
How do we combine the individual expected losses to get the total expected loss?
Exeedance Probability Methodology
  Uses different exceedance probabilities (EP)
  Probability of exceeding certain amount of loss
    If an earthquake happens – Conditional EP
    Due to at least one earthquake in a year – Occurrence EP
    Due to all the earthquakes in a year – Aggregate EP
  Average Annual Loss
    Expected loss in a given year.
    Area under the AEP Curve
Source: Exceedance Probability Methodology, 2010
Fig. Typical AEP Curve for a structure

## Slide 7: Resilience of Bridges
Can we incorporate loss with the functionality during recovery, and recovery time into a useful parameter?
Resilience
  Capability to sustain a level of functionality after damage
  Takes into account how often the event can occur in structure’s lifetime
  Normalized function
Source: Cimellaro et al., 2006
Fig. Typical Recovery Curve for a structure

## Slide 8: Case Study
Parameters | Golden Gate Bridge | San Mateo-Hayward Bridge | Dumbarton Bridge
Location on Map | 1 | 2 | 3
Replacement Value (2019 $) | $ 523 Million | $ 418 Million | $ 182 Million
Sources | Color On Map | Source Set | Return Period
San Andreas (Peninsula) | Red | UC33brAvg_FM31, UC33brAvg_FM32 | 475, 975, 2475
San Gregorio (North) | Orange | UC33brAvg_FM31, UC33brAvg_FM32 | 475, 975
Fig. Location of Bridges and common faults affecting them

## Slide 9: Result and Conclusion
Parameters | Golden Gate Bridge | San Mateo-Hayward Bridge | Dumbarton Bridge
Hazard Range for the location SA(1.0s) (g) | 0.18 – 0.24 | 0.10 – 0.18 | 0.10 – 0.18
Average Annual Loss | $ 93,524.57 | $ 50,093.06 | $ 10,439.35
Resilience | 2.9403 | 2.9651 | 2.9927
Priority of Retrofit
Highest AAL First : Golden Gate -> San Mateo-Hayward -> Dumbarton
Lowest Resilience First : Golden Gate -> San Mateo-Hayward -> Dumbarton
Fig. AEP Curves for the three bridges

## Slide 10: Scope of Future Work
Integration of Network analysis and effect on Traffic Flow
  Effect of a bridge’s damage on the traffic flow
  Indirect costs associated with detours
Inclusion of environmental aspects
  Increased Carbon-footprint due to detours
  Environmental impact due to reconstruction
Integration of Bridge’s Age and past Retrofits
  Effect on bridge’s strength due to age and retrofit
Expansion to other critical structures
  Water supply system, waste water system, hospitals